Computer Electronics
Circuit Theory and Electronics Fundamentals
Lab 2: RC Circuit Analysis

---
The RC circuit
1
2
3
v_s( t) = V_s u(-t) + sin( 2 %pi f t ) u( t) newline newline u( t ) = left lbrace {binom{0, t < 0}{1, t >= 0} } right none
R1
R2
+
Vb
-
+
-
R3
Ib = Kb Vb
5
6
R4
R5
+
-
Ic
R6
Id
C
Vd = Kd Id
7
8
R7

---
Simulation Analysis
1. Simulate the operating point for t<0, to obtain the voltages in all nodes and the currents in all branches. Print a table with the results.
2. Simulate the operating point for vs(0)=0, replacing the capacitor with a voltage source Vx = V(6)-V(8), where V(6) and V(8) are the voltages in nodes 6 and 8 as obtained in 1). Explain why you need this step. Print a table with the results.
3. Simulate the natural response of the circuit, using the boundary conditions V(6) and V(8) as obtained in 2) (use Ngspice directive .ic V(6)=... v(9)=...). Use Ngpice’s transient analysis mode to get v6(t) in the interval [0, 20] ms. Plot the result.
4. Simulate the natural and forced response on node 6 by repeating step 3) with vs(t) as given in Fig. 1 and f=1kHz. Plot both the stimulus and the response.
5. Simulate the frequency response in node 6 (frequency logscale, magnitude in dB, phase in degrees) for the frequency range 0.1 Hz to 1 MHz. Plot both vs(f) and v6(f) in the same figure and explain how and why they differ.

---
Theoretical Analysis
1. Use the nodal method to determine the voltages in all nodes and currents in all branches for t<0. Print a table with the results.
2. Determine the equivalent resistance Req as seen from the capacitor terminals. Suggestion: make Vs=0 and replace the capacitor with a voltage source Vx= V(6)-V(8), where V(6) and V(8) are the voltages in nodes 6 and 8 as obtained in 1); run nodal analysis to determine the current Ix supplied by Vx; compute the equivalent resistor as Req = Vx/Ix,and the time constant. Explain why you need this procedure, and print a table with the computed results.
3. With the results obtained in 2), determine the natural solution v6n(t), in the interval [0, 20] ms, using the capacitor voltage Vx for t<0 as the initial condition. Plot the result, identifying all axes, signals displayed and units used.
4. Determine the forced solution v6f(t) in the same interval. Suggestion: use a phasor voltage source Vs; replace C with its impedance ZC; run nodal analysis to determine the phasor voltages in all nodes. Print a table with the results.
5. Determine the final total solution v6(t), converting the phasors to real time functions for f=1KHz, and superimposing the natural and forced solutions. Plot both vs(t) and v6(t) in the same figure in the interval [-5, 20] ms.
6. Determine the frequency responses vc(f)=v6(f)-v8(f), and v6(f) (frequency logscale magnitude in dB, phase in degrees) for frequency range 0.1 Hz to 1 MHz. Plot vs(f), vc(f) and v6(f) in the same figure and explain how and why they differ.

---
Lab report
1. The Python script, t2_datagen.m output should be redirected to a file data.txt using bash’s “>” facility.
2. The octave script should read and use the data file data.txt, and output a data file for Ngspice (directive .include). Use file I/O functions such as fprintf and fscanf.
3. Ideally, generating a new data set with a different student number and re-running the top Makefile should produce consistent results.
4. Produce all tables and plots required in the simulation and analysis sections
5. Compare Octave and Ngspice results side by side looking for exactness or discrepancy, and explaining both. Read the repository’s README file.